## Slide 1: Force Analysis Of Holonomic Wheels
Nex+Gen Griffin Robotics FTC Team 7582
Cameron Pase
Douglas Pase, dmpase@gmail.com

## Slide 2
Bearing 0°
velocity 2
FL: -√2/2
FR: +√2/2
BR: +√2/2
BL: -√2/2
0°
90°
180°
270°
45°
135°
225°
315°
+√2/2
+√2/2
-√2/2
-√2/2
√2
√2
FL
BL
BR
FR

## Slide 3
Bearing 45°
velocity 2
FL: -1
FR: 0
BR: +1
BL: 0
0°
90°
180°
270°
45°
135°
225°
315°
0
+1
-1
0
FL
BL
BR
FR

## Slide 4
-√2/2
+√2/2
-√2/2
+√2/2
Bearing 90°
velocity 2
FL: -√2/2
FR: -√2/2
BR: +√2/2
BL: +√2/2
0°
90°
180°
270°
45°
135°
225°
315°
√2
√2
FL
BL
BR
FR

## Slide 5
Bearing 135°
velocity 2
FL: 0
FR: -1
BR: 0
BL: +1
0°
90°
180°
270°
45°
135°
225°
315°
-1
0
0
+1
FL
BL
BR
FR

## Slide 6
Bearing 180°
velocity 2
FL: +√2/2
FR: -√2/2
BR: -√2/2
BL: +√2/2
0°
90°
180°
270°
45°
135°
225°
315°
-√2/2
-√2/2
+√2/2
+√2/2
√2
√2
FL
BL
BR
FR

## Slide 7
Bearing 225°
velocity 2
FL: +1
FR: 0
BR: -1
BL: 0
0°
90°
180°
270°
45°
135°
225°
315°
0
-1
+1
0
FL
BL
BR
FR

## Slide 8
Bearing 270°
velocity 2
FL: +√2/2
FR: +√2/2
BR: -√2/2
BL: -√2/2
0°
90°
180°
270°
45°
135°
225°
315°
+√2/2
-√2/2
+√2/2
-√2/2
√2
√2
FL
BL
BR
FR

## Slide 9
Bearing 315°
velocity 2
FL: 0
FR: +1
BR: 0
BL: -1
0°
90°
180°
270°
45°
135°
225°
315°
+1
0
0
-1
FL
BL
BR
FR

## Slide 10: Computing Motor Power From A Bearing
Bearing | 0° | 45° | 90° | 135° | 180° | 225° | 270° | 315° | Power
Front Left | -√2/2 | -1 | -√2/2 | 0 | +√2/2 | +1 | +√2/2 | 0 | -sin(b+45°)
Front Right | +√2/2 | 0 | -√2/2 | -1 | -√2/2 | 0 | +√2/2 | +1 | cos(b+45°)
Back Right | +√2/2 | +1 | +√2/2 | 0 | -√2/2 | -1 | -√2/2 | 0 | sin(b+45°)
Back Left | -√2/2 | 0 | +√2/2 | +1 | +√2/2 | 0 | -√2/2 | -1 | -cos(b+45°)
sin(b+45°) | +√2/2 | +1 | +√2/2 | 0 | -√2/2 | -1 | -√2/2 | 0 | 
cos(b+45°) | +√2/2 | 0 | -√2/2 | -1 | -√2/2 | 0 | +√2/2 | +1 | 

## Slide 11: Rotation

## Slide 12
Rotate Right
velocity 2
FL: -1
FR: -1
BR: -1
BL: -1
0°
90°
180°
270°
45°
135°
225°
315°
BR
FL
BL
FR
-1
-1
-1
-1

## Slide 13
Rotate Left
velocity 2
FL: +1
FR: +1
BR: +1
BL: +1
0°
90°
180°
270°
45°
135°
225°
315°
BR
FL
BL
FR
+1
+1
+1
+1

## Slide 14: Joystick Calculations

## Slide 15: The Gamepad Joysticks
Each gamepad has two joysticks, left and right
Joysticks have two axes, x and y
Each axis is given a name that reflects the gamepad, joystick and axis
  double gamepad1.left_stick_x
  double gamepad1.left_stick_y
  double gamepad2.right_stick_x
  …
We can read each axis value individually using that name
Left Joystick
Right
Joystick

## Slide 16: Joystick Conventions
Joysticks follow the conventions of computer graphics displays
The x axis increases from left to right, like in mathematics
But the y axis is upside down, it increases from top to bottom, which is the opposite of math
The joystick x and y have a range of -1.0 to +1.0
We can use the values of x and y to compute the direction the driver is telling the robot to go
x
+1.0
-1.0
y
+1.0
Active
Clipped
-1.0

## Slide 17: Trigonometry Review
Start with a unit circle (radius=1)
For some angle a …
x = cos a
y = sin a
Pythagorean theorem says,
x2 + y2 = (cos a)2 + (sin a)2 = 1
+1.0
-1.0
y
-1.0
+1.0
a
x
(cos a, sin a)

## Slide 18: The Math.atan2(y, x) function
If you know a point (x, y) on the line, you can find the angle a to the x-axis
a = Math.atan2(y, x)
Notice a is the angle from the x-axis to the line, in radians
We can use this to find the direction the joystick is pointing, but we have to convert a to a bearing, in degrees
+1.0
-1.0
y
-1.0
+1.0
a
x
(x, y)

## Slide 19: Comparing a to a Bearing
a
0°
90°
180°
270°
45°
135°
225°
315°
0 (0°)
p/4 (45°)
p/2 (90°)
3p/4 (135°)
p (180°)
-3p/4 (-135°)
-p/2 (-90°)
-p/4 (-45°)
0°
45°
90°
135°
180°
225°
270°
315°
a (deg.)
bearing
bearing

## Slide 20: Comparing a to a Bearing
a
a is in radians
a is an angle from the x-axis
a increases in a counterclockwise direction
Bearing
bearing is in degrees
bearing is an angle from the y-axis
bearing increases in a clockwise direction

## Slide 21: Converting Between a and a Bearing
x = gamepad1.left_stick_x
y = - gamepad1.left_stick_y
= Math.atan2(y, x)
To get the bearing in degrees
bearing = 90° – 180° * a / p
Math.sin() and Math.cos() need the bearing in radians
radians = p * bearing / 180°

## Slide 22: The Final Step
Motor output should be proportional to how far the joystick is moved
  All the way forward means as fast as possible
  A little push means a little speed
The length (distance from the center to the joystick position) can be calculated from x and y using the Pythagorean Theorem
length = = Math.sqrt(x*x+y*y)
The length should never be greater than +1.0 or the motors will throw an exception
length = Math.min(length, 1.0)

## Slide 23
x
+1.0
-1.0
y
+1.0
Active
Clipped
a
0°
90°
180°
270°
45°
135°
225°
315°
0 (0°)
p/4 (45°)
p/2 (90°)
3p/4 (135°)
p (180°)
-3p/4 (-135°)
-p/2 (-90°)
-p/4 (-45°)
x = gamepad1.left_stick_x
y = -gamepad1.left_stick_y
a = Math.atan2(y, x)
bearing = 90° - a * 180°/p
length = √(x2+y2)
speed = min( length, 1.0 )
-1.0
0°
45°
90°
135°
180°
225°
270°
315°
a (deg.) bearing
bearing
bearing

## Slide 24: Questions?