## Slide 1: FTC Java Programming Topics
Nex+Gen Griffin Robotics FTC Team 7582
Douglas Pase, dmpase@gmail.com

## Slide 2: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 3: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 4: Robot Architecture
Configuration File
Device Name
Device Type
Port ID
Driver Station
Robot Controller
Game Pad
WiFi Direct
Motors
Sensors
Robot Program
Servos

## Slide 5: Linear Programming Model
Easiest to understand
Most like a typical Java application
  Sequential execution from start to finish – do task A, task B, task C, …
  When the last task is done, the robot stops
Best suited for autonomous operation
  Autonomous mode executes tasks in sequence, just like Linear Model
Phases are not built into the model
  Init, wait, main and stop operations must be explicitly coded into the program

## Slide 6: Linear Code
@Autonomous(name="Autonomous Mode", group="Autonomous") // name used on driver station
public class Autonomous_Linear extends LinearOpMode { // superclass must be LinearOpMode
private ElapsedTime runtime = new ElapsedTime(); // timer object
@Override // java safety feature
public void runOpMode() { // required, your robot code
… // initialization section
waitForStart(); // wait for start to be pressed
// main section, robot does work
runtime.reset(); // reset robot clock
if (opModeIsActive()) { // check if “stop” was signaled
… // do next leg of operation
} // …
… // stop section, shut down robot
}
}

## Slide 7: Initialization Section
runOpMode() is called when “Init” is pressed on the Driver Station
Immediately begins with the initialization of the robot
Turn on all devices
Each device (motor, servo, sensor) must be activated individually
Activating a device places it into a known state, ready for use
Extends from the start of the runOpMode() function to waitForStart()

## Slide 8: Wait Section
Waits for the operator to press “Play” on the Driver Station
Implemented on the robot with the call to waitForStart()
When waitForStart() returns, “Play” has been pressed

## Slide 9: Main Section
Begins immediately following waitForStart()
Performs the real work of your autonomous mode
Robot timer should be restarted at the beginning
Each leg should check whether “Stop” has been pressed
When opModeIsActive() returns false, “Stop” has been pressed

## Slide 10: Stop Section
No distinct marker separating “Main” and “Stop” sections
Begins after the last leg of the “Main” section, or whenever the real work is complete
Shuts-down the robot components (e.g., motors, servos, sensors)
When the runOpMode() routine exits, the robot stops

## Slide 11: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 12: Robot Architecture
Configuration File
Device Name
Device Type
Port ID
Driver Station
Robot Controller
Game Pad
WiFi Direct
Motors
Sensors
Robot Program
Servos

## Slide 13: Iterative Programming Model
Most suitable for driver operation
Separates the operation into “init”, “loop” and “stop” sections
  Two additional sections, “init_loop” and “start”, are also available
Sections are implemented as individual routines
Unused routines may be inherited from the OpMode superclass
Uses “polling” for the main (loop) phase (explained later)

## Slide 14: Iterative Code
@TeleOp(name=“Driver Mode", group="Iterative Opmode") // name used on driver station
public class Driver_Iterative extends OpMode { // superclass must be OpMode
private ElapsedTime runtime = new ElapsedTime(); // timer object
@Override
public void init() { // initialization section
…
}
@Override
public void init_loop() { } // initialization loop section
@Override
public void start() { runtime.reset(); } // start section
@Override
public void loop() { // loop section
…
}
@Override
public void stop() { // stop section
…
}
}

## Slide 15: Initialization Section
Called once after “Init” is pressed on the Driver Station
Initialization code is placed in the init() routine
Turn on all devices in the robot
Each device (motor, servo, sensor) must be activated individually
Activating a device places it into a known state, ready for use
Works similar to the initialization section of a Linear Op Mode
Times out if it does not finish in less than 4 seconds
Timing out aborts the program and crashes the robot

## Slide 16: Init_loop
Executes repeatedly after init() and before start()
Useful for keeping devices “warm” between initialization and play
Code is placed in the init_loop() routine
Not often used or needed
May also time out if not completed quickly

## Slide 17: Start
Executes once after the driver presses “Play” on the driver station
Used to reset the robot clock at the beginning of play
May also time out if not completed quickly

## Slide 18: Loop
Executes repeatedly after “Play” is pressed
Continues to execute until “Stop” is pressed
Normal operation often follows this pattern:
  Read input from the game pads, sensors, and encoders
  Compute changes to the motor and servo power settings
  Set the new power levels for the motors and servos
Executed about every 1/10th second (polling)
Times out if it does not finish in less than 4 seconds
Timing out aborts the program and crashes the robot

## Slide 19: Stop
Executes once after the “Stop” button has been pressed
Shuts-down the robot components (e.g., motors, servos, sensors)
When stop() exits, the robot program terminates

## Slide 20: Telemetry
Telemetry sends data from the robot to the driver station for display
The telemetry object is inherited from OpMode or LinearOpMode
telemetry.addData(String caption, String value)
telemetry.addData(String caption, String format, args…)
telemetry.update()
  In Linear Op Mode, update is needed to display data on the driver station
  In Iterative Op Mode, update occurs automatically at the end of each loop

## Slide 21: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 22: Robot Architecture
Configuration File
Device Name
Device Type
Port ID
Driver Station
Robot Controller
Game Pad
WiFi Direct
Motors
Sensors
Robot Program
Servos

## Slide 23: Initializing Robot Devices In Java
All devices (motors, servos, sensors) are represented as Java objects
  Motors are represented as objects of type DcMotor
  Servos are represented as objects of type Servo
  Continuous rotation servos are objects of type CRServo
  REV color sensors are objects of type ColorSensor
  MR ultrasonic range sensors are objects of type DistanceSensor
Import device types from com.qualcomm.robotcore.hardware.*
Declare devices as class objects with initial values of null
  DcMotor dcm = null;
Initialize devices in init() or initialization section of the robot program
Use hardwareMap.get() to initialize the objects
  hardwareMap is a class object of the parent class OpMode or LinearOpMode
  DcMotor dcm = hardwareMap.get(DcMotor.class, “xyz”);
  Where “xyz” is the name of the device as it is used in the configuration file
  DcMotor.class is the Java type of the device object

## Slide 24: Configuration Files
Bridge the gap between devices in your program and actual hardware
Associate a device name (used by the program) with a device type and a port identifier (used by the hardware)
Each time you call hardwareMap.get():
  The robot program asks the FTC software for a device by its name and type
  The FTC software checks the name and type against the configuration file
  If all is well, it returns a handle that can talk to the hardware on that port
  OR, it throws an Exception when the name is missing, the type doesn’t match, or there is some other problem talking to the hardware device on that port

## Slide 25: DcMotors – Run Using Encoder
DcMotor drive = null; // class declaration
// initialization
drive = hardwareMap.get(DcMotor.class, “drive name”);
drive.setDirection(DcMotor.Direction.FORWARD);
drive.setPower(0);
drive.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
drive.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
drive.setPower(DRIVE_POWER); // use, -1.0 < power < 1.0

## Slide 26: DcMotors – Run To Position
DcMotor lift = null; // class declaration
// initialization
lift = hardwareMap.get(DcMotor.class, “lift name”);
lift.setDirection(DcMotor.Direction.FORWARD);
lift.setPower(0);
lift.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
lift.setMode(DcMotor.RunMode.RUN_TO_POSITION);
lift.setTargetPosition(target); // use, target = encoder value
lift.setPower(LIFT_POWER); // -1.0 < power < 1.0

## Slide 27: Servos
Servo tail = null; // class declaration
// initialization
tail = hardwareMap.get(Servo.class, “servo name”);
tail.setDirection(Servo.Direction.FORWARD);
tail.setPosition(TAIL_POSITION); // use, -1.0 < position < 1.0

## Slide 28: REV Color/Range Sensor
ColorSensor color = null; // class declaration
DistanceSensor range = null;
// initialization
color = hardwareMap.get(ColorSensor.class, “c/r sensor name”);
range = hardwareMap.get(DistanceSensor.class, “c/r sensor name”);
double alpha = color.alpha(); // use
double red = color.red();
double green = color.green();
double blue = color.blue();
double range = range.getDistance(DistanceUnit.INCH);

## Slide 29: Modern Robotics Ultrasonic Range Sensor
DistanceSensor sensor = null; // class declaration
// initialization
sensor = hardwareMap.get(DistanceSensor.class, “sensor name”);
// use
double range = sensor.getDistance(DistanceUnit.INCH);

## Slide 30: Fields In gamepad1 & gamepad2
Field | Type | Field | Type | Field | Type
a | boolean | left_bumper | boolean | left_stick_x | double
b | boolean | right_bumper | boolean | left_stick_y | double
x | boolean | left_stick_button | boolean | right_stick_x | double
y | boolean | right_stick_button | boolean | right_stick_y | double
dpad_up | boolean | start | boolean | left_trigger | double
dpad_down | boolean | back | boolean | right_trigger | double
dpad_left | boolean | guide | boolean |  | 
dpad_right | boolean |  |  |  | 
To use, say: gamepadk.field, for example, gamepad1.right_bumper

## Slide 31: Analog Sensor (E.g., Pololu IR Sensor)
AnalogInput sensor = null; // class declaration
// initialization
sensor = hardwareMap.get(AnalogInput.class, “sensor name”);
// use
double voltage = sensor.getVoltage();
// you must then convert the
// voltage to a distance or
// other appropriate value

## Slide 32: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 33: Why use abstraction and inheritance?
Your team has two different ideas you want to try, like two types of drives
You want to try both out and compare them side by side
You copy your Op Mode and make changes to the hardware
Next you find a bug and need to update the controls of both robots…
With every change you make, it gets harder to keep them the same
Or…
Your Op Mode is nearly done when you find some better hardware
To change out the old hardware you need to find every place that touches the old and replace it with new controls. It is scattered everywhere!
There must be a better way! (There is.)

## Slide 34: What is inheritance?
Java supports an idea called inheritance
Two classes may have a parent-child relationship
A child class (or subclass) inherits all of the data and subroutines from its parent class (or superclass)
Examples you have already seen
  Your Driver Op Mode inherits from class OpMode
  Your Autonomous Op Mode inherits from class LinearOpMode
  In other words, your Driver Op Mode is a subclass of superclass OpMode and your Autonomous Op Mode is a subclass of superclass LinearOpMode
Everything in the superclass (parent) is also in the subclass (child)

## Slide 35: Inheritance Example
  public class Parent { // parent class (or superclass)
  public void move(double bearing, double speed) {
  …
  }
  }
  public class Child extends Parent { // child class (or subclass)
  // Child can use move from Parent and spin from Child
  public void spin(double speed) {
  …
  }
  }

## Slide 36: Override Example
Functions in the child class can override functions in the parent, too
  public class Parent { // parent class (or superclass)
  public void move(double bearing, double speed) {
  …
  }
  }
  public class Child extends Parent { // child class (or subclass)
  // Child can use move from Child or super.move from Parent
  @Override
  public void move(double bearing, double speed) {
  …
  }
  }

## Slide 37: Abstract Functions And Classes
Functions can be declared abstract in a parent class
Abstract functions are declared but not implemented
Declaring a function abstract says the child must implement it, e.g.,
public abstract void move(double bearing, double speed);
Any class that contains an abstract function must be declared abstract
Any child of an abstract class must implement the abstract function

## Slide 38: Abstract Class Example
  public abstract class AbstractParent { // abstract parent class
  public abstract void move(double bearing, double speed);
  }
  public class Child extends AbstractParent { // child class
  @Override
  public void move(double bearing, double speed) {
  …
  }
  }

## Slide 39: Objects Of Abstract Type
Variables of abstract classes can only be assigned child classes
  AbstractParent data = new Child();
Variables of abstract classes may use only routines and data from the abstract class (or its parents)

## Slide 40: This sounds complicated, how do I use it?
Instead of putting everything together in one Op Mode class…
Create an abstract motion class that defines what your drive motors do
Create a non-abstract child of the abstract motion class (from 1) that
  Implements the abstract functions of the parent class, and
  Talks to the real hardware
Create an abstract parent Op Mode that
  Takes input from the gamepads, sensors, etc., and
  Uses the abstract motion class (step 1) to define when and how the robot moves
Create a child class of the abstract Op Mode that
  Sets the abstract motor object to the motor class (from step 2)

## Slide 41: A Better Robot Design
Abstract Op Mode Class
Runnable Op Mode Class
Runnable Motion Class
Abstract Motion Class
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
(hardwareMap lives here)
(hardwareMap is used here)
(pointer to FTC Op Mode is here)
Has-A
superclass of Runnable Motion
subclass of FTC Op Mode
subclass of Abstract Op Mode
superclass of Abstract Op Mode
subclass of Abstract Motion
superclass of Runnable Op Mode

## Slide 42: It sounds like more work, how is this easier?
You write your Op Mode in terms of what the motors do for you (e.g., move forward, etc.) instead of how you have to talk to the hardware.
  Defining your robot program in terms of what it does instead of how it works makes it easier to understand and simpler to code.
To support two different types of robot, re-write only those parts that are different, e.g., write a new runnable motion class (step 2) and create a new runnable Op Mode class (step 4).
  The abstract Op Mode and abstract motion class are shared.
  This is much easier than re-writing the Op Mode each time the hardware changes.
Replacing old hardware with more advanced (e.g., tank drive with holonomic drive) is easier because you change it in only one place.
  Change the runnable motion class from step 2, the rest stays the same.

## Slide 43: Example – Griffin Robot With Claw
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 44: Griffin Robot With Claw - GriffinDriverOp
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 45: Griffin Driver Op Mode
public class GriffinDriverOp extends OpMode {
public GriffinMove drive = null;
public GriffinClaw claw = null;
private ElapsedTime runtime = new ElapsedTime();
@Override
public void init() {
. . .
}
@Override
public void start() { runtime.reset(); }
@Override
public void loop() {
. . .
}
@Override
public void stop() {
. . .
}
}

## Slide 46: Griffin Driver Op Mode - Init
. . .
@Override
public void init() {
telemetry.addData("Status", "Initializing Drive.");
drive.init();
telemetry.addData("Status", "Initializing Claw.");
claw.init();
telemetry.addData("Status", "Initialization Complete.");
}
. . .

## Slide 47: Griffin Driver Op Mode - Loop
. . .
@Override
public void loop() {
if (gamepad1.dpad_up) {
drive.move( 0.0, 0.5);
} else if (gamepad1.dpad_right) {
drive.move( 90.0, 0.5);
} else if (gamepad1.dpad_down) {
drive.move(180.0, 0.5);
} else if (gamepad1.dpad_right) {
drive.move(270.0, 0.5);
} else {
drive.move( 0.0, 0.0);
}
if (gamepad1.x) {
claw.open();
} else if (gamepad1.b) {
claw.close();
}
}
. . .

## Slide 48: Griffin Driver Op Mode - Stop
. . .
@Override
public void stop() {
telemetry.addData("Status", “Stopping Drive.");
drive.stop();
telemetry.addData("Status", “Stopping Claw.");
claw.stop();
telemetry.addData("Status", “Robot Stopped.");
}
}

## Slide 49: Griffin Robot With Claw - GriffinMove
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 50: Griffin Move
public class GriffinMove {
protected OpMode op_mode = null;
public abstract void init();
public abstract void move(double bearing, double speed);
public abstract void stop();
public GriffinMove(OpMode op) {
op_mode = op; // save a pointer to the FTC Op Mode
}
}

## Slide 51: Griffin Robot With Claw - LionMove
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 52: Lion Move
public class LionMove extends GriffinMove {
public LionMove(OpMode op) {
super(op);
}
private DcMotor front_left = null;
private DcMotor front_right = null;
private DcMotor back_right = null;
private DcMotor back_left = null;
public void init() {
. . .
}
public void move(double bearing, double power) {
. . .
}
public void stop() {
. . .
}
}

## Slide 53: Lion Move – Init
public void init() {
front_left = op_mode.hardwareMap.get(DcMotor.class, “front left”);
front_left.setDirection(DcMotor.Direction.FORWARD);
front_left.setPower(0);
front_left.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
front_left.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
front_right = op_mode.hardwareMap.get(DcMotor.class, “front right”);
front_right.setDirection(DcMotor.Direction.FORWARD);
front_right.setPower(0);
front_right.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
front_right.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
back_right = op_mode.hardwareMap.get(DcMotor.class, “back right”);
back_right.setDirection(DcMotor.Direction.FORWARD);
back_right.setPower(0);
back_right.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
back_right.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
back_left = op_mode.hardwareMap.get(DcMotor.class, “back left”);
back_left.setDirection(DcMotor.Direction.FORWARD);
back_left.setPower(0);
back_left.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
back_left.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
}

## Slide 54: Lion Move – Move
public void move(double bearing, double power) {
if (315 < bearing || bearing < 45) { // go forward
front_left.setPower (-power);
front_right.setPower( power);
back_right.setPower ( power);
back_left.setPower (-power);
} else if (45 < bearing && bearing < 135) { // go right
front_left.setPower (-power);
front_right.setPower(-power);
back_right.setPower ( power);
back_left.setPower ( power);
} else if (135 < bearing && bearing < 225) { // go backward
front_left.setPower ( power);
front_right.setPower(-power);
back_right.setPower (-power);
back_left.setPower ( power);
} else if (225 < bearing && bearing < 315) { // go left
front_left.setPower ( power);
front_right.setPower( power);
back_right.setPower (-power);
back_left.setPower (-power);
}
}

## Slide 55: Lion Move – Stop
public void stop() {
front_left.setPower (0);
front_right.setPower(0);
back_right.setPower (0);
back_left.setPower (0);
}

## Slide 56: Griffin Robot With Claw - GriffinClaw
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 57: Griffin Claw
public class GriffinClaw {
public OpMode op_mode = null;
public abstract void init();
public abstract void open();
public abstract void close();
public abstract void stop();
public GriffinClaw(OpMode op) {
op_mode = op; // save a pointer to the FTC Op Mode
}
}

## Slide 58: Griffin Robot With Claw - LionClaw
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 59: Lion Claw
public class LionClaw extends GriffinClaw {
public LionClaw(OpMode op) {
super(op);
}
private Servo claw = null;
public void init() {
claw = hardwareMap.get(Servo.class, “claw”);
claw.setDirection(Servo.Direction.FORWARD);
}
public void open() {
claw.setPosition(1.0);
}
public void close() {
claw.setPosition(0.0);
}
public void stop() {
close();
}
}

## Slide 60: Griffin Robot With Claw - LionDriverOp
GriffinDriverOp
LionDriverOp
LionMove
GriffinMove
Has-A
Is-A
Is-A
FTC Op Mode
Is-A
LionClaw
GriffinClaw
Is-A
Has-A

## Slide 61: Lion Driver Op
@TeleOp(name="Lion Driver Op Mode", group="Iterative Opmode")
public class LionDriverOp extends GriffinDriverOp {
public LionDriverOp() {
drive = new LionMove(this);
claw = new LionClaw(this);
}
}

## Slide 62: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 63: What could possibly go wrong?
You forget to initialize a device
You use the wrong name for a device
You use the wrong device type (e.g., you call a sensor a servo)
The device isn’t plugged in
The device breaks

## Slide 64: What happens when something goes wrong?
In every case your program stops what it’s doing and “throws an exception”
If you do nothing, your program will abort with a nasty error message
If you catch the exception, you can deal with it and continue
The way we catch exceptions is with a try/catch block

## Slide 65: Catching An Exception
try {
drive = hardwareMap.get(DcMotor.class, “drive name”);
drive.setDirection(DcMotor.Direction.FORWARD);
drive.setPower(0);
drive.setMode(DcMotor.RunMode.STOP_AND_RESET_ENCODER);
drive.setMode(DcMotor.RunMode.RUN_USING_ENCODER);
} catch (Exception e) {
drive = null;
}
. . .
if (drive != null) {
drive.setPower(power);
}

## Slide 66: Agenda
1:00 – 1:55: Robot Programming Basics
  Linear (Autonomous) Programming Model
  Iterative (Driver) Programming Model
  Talking To The Robot
2:00 – 2:55: Advanced Programming
  Using Inheritance And Abstraction To Support Multiple Robots
  Using Exceptions To Handle Hardware Failures
3:00 – 3:55: Special Topics
  Open Discussion And Q/A

## Slide 67: Open Discussion and Q/A